## Slide 1: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 2: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 3: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 4: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 5
IPv4 address has two components, the network part and the host part.
In fact IPv4 address , is a combination of IPv4 address and Subnet mask
The purpose of subnet mask is to identify which part is the network part and which part is the host part.
Subnet mask is a 32 bit number where all the bits of the network part are represented as 1 and all the bits of the host part are represented as 0.
For example, for a Class C Network, 192.168.10.0, the address part and the subnet mask is 255.255.255.0
What is Subnet Mask?

## Slide 6
A logical, visible subdivision of an IP network is called subnet or subnetwork.
  It is created by dividing the host identifier
Subnetting is the practice of dividing a network into two or more networks.
In subnetting, a class A or class B or class C block is divided into several subnets (each subnet with larger prefix length than the original network).
For example, divide the class A into four subnets, then each subnet will have prefix length as 10 (take two bits from host id part in order to obtain subnets).
Subnet and Subnetting

## Slide 7
Subnetting is done by taking the bits from host part and adding it to the network part
Remember the following [as already covered]
If all the bits in the host part are "0", that represents the network id (network address)
If all the bits in the host part are "0" except the last bit, it is the first usable IPv4 address
If all the bits in the host part are "1" except the last bit, it is the last usable IPv4 address
If all the bits in the host part are "1", that represents the broadcast
Subnetting

## Slide 8
Consider class c network 192.168.10.0 (subnet mask is 255.255.255.0)
If we include one bit from the host part to the network part, the subnet mask changes into 255.255.255.128.
The single bit can have two values in last octet, either 0 or 1 (so we can get two subnets with a single bit subnetting)
11000000.10101000.00001010.0 | 0000000 11111111.11111111.11111111.1 | 0000000
So the network 192.168.10.0 is divided into two networks,
  each network has 128 total addresses of which 126 are usable
    two are used in each subnet to represent the network address and broadcast address.
Class C – 1 bit subnetting

## Slide 9
Class C – 1 bit subnetting
SN No. | Description | Binaries | Decimal
1 | Network Address | 11000000.10101000.00001010.00000000 | 192.168.10.0
 | First usable address | 11000000.10101000.00001010.00000001 | 192.168.10.1
 | Last usable address | 11000000.10101000.00001010.01111110 | 192.168.10.126
 | Broadcast Address | 11000000.10101000.00001010.01111111 | 192.168.10.127
2 | Network Address | 11000000.10101000.00001010.10000000 | 192.168.10.128
 | First usable address | 11000000.10101000.00001010.10000001 | 192.168.10.129
 | Last usable address | 11000000.10101000.00001010.11111110 | 192.168.10.254
 | Broadcast Address | 11000000.10101000.00001010.11111111 | 192.168.10.255

## Slide 10
Class C – 2 bit subnetting
SN No. | Description | Binaries | Decimal
1 | NA | 11000000.10101000.00001010.00000000 | 192.168.10.0
 | 1st | 11000000.10101000.00001010.00000001 | 192.168.10.1
 | Last | 11000000.10101000.00001010.00111110 | 192.168.10.62
 | BA | 11000000.10101000.00001010.00111111 | 192.168.10.63
2 | NA | 11000000.10101000.00001010.01000000 | 192.168.10.64
 | 1st | 11000000.10101000.00001010.01000001 | 192.168.10.65
 | Last | 11000000.10101000.00001010.01111110 | 192.168.10.126
 | BA | 11000000.10101000.00001010.01111111 | 192.168.10.127
3 | NA | 11000000.10101000.00001010.10000000 | 192.168.10.128
 | 1st | 11000000.10101000.00001010.10000001 | 192.168.10.129
 | Last | 11000000.10101000.00001010.10111110 | 192.168.10.190
 | BA | 11000000.10101000.00001010.10111111 | 192.168.10.191
4 | NA | 11000000.10101000.00001010.11000000 | 192.168.10.192
 | 1st | 11000000.10101000.00001010.11000001 | 192.168.10.193
 | Last | 11000000.10101000.00001010.11111110 | 192.168.10.254
 | BA | 11000000.10101000.00001010.11111111 | 192.168.10.255

## Slide 11
Class C – 3 bit subnetting
SN No. | Description | Binaries | Decimal
1 | NA | 11000000.10101000.00001010.00000000 | 192.168.10.0
 | 1st | 11000000.10101000.00001010.00000001 | 192.168.10.1
 | Last | 11000000.10101000.00001010.00011110 | 192.168.10.30
 | BA | 11000000.10101000.00001010.00011111 | 192.168.10.31
2 | NA | 11000000.10101000.00001010.00100000 | 192.168.10.32
 | 1st | 11000000.10101000.00001010.00100001 | 192.168.10.33
 | Last | 11000000.10101000.00001010.00111110 | 192.168.10.62
 | BA | 11000000.10101000.00001010.00111111 | 192.168.10.63
……………. |  |  | 
8 | NA | 11000000.10101000.00001010.11100000 | 192.168.10.224
 | 1st | 11000000.10101000.00001010.11100001 | 192.168.10.225
 | Last | 11000000.10101000.00001010.11111110 | 192.168.10.254
 | BA | 11000000.10101000.00001010.11111111 | 192.168.10.255

## Slide 12: ASSIGNMENT 3

## Slide 13: Task-C
Apply 1 bit subnetting to
  201.65.71.0
  What is Network Address?
  What is broadcast address?
  No. of blocks?

## Slide 14: Task-A
Apply 2 bit subnetting to
  219.30.5.27
  No. of blocks?
  What is Network Address?
  What is 1st usable address?
  What is last usable address?
  What is broadcast address?

## Slide 15: Solution- Task A
IP Address: | 219.30.5.27
Network Address: | 219.30.5.0
Usable Host IP Range: | 219.30.5.1 - 219.30.5.62
Broadcast Address: | 219.30.5.63
Total Number of Hosts: | 64
Number of Usable Hosts: | 62
219.30.5.0 | 219.30.5.1 - 219.30.5.62 | 219.30.5.63
219.30.5.64 | 219.30.5.65 - 219.30.5.126 | 219.30.5.127
219.30.5.128 | 219.30.5.129 - 219.30.5.190 | 219.30.5.191
219.30.5.192 | 219.30.5.193 - 219.30.5.254 | 219.30.5.255

## Slide 16
Consider class B network 172.16.0.0 (subnet mask is 255.255.0.0)
If we include one bit from the host part to the network part, the subnet mask changes into 255.255.128.0.
The single bit can have two values in last octet, either 0 or 1 (so we can get two subnets with a single bit subnetting)
10101100.00010000.0 | 0000000.00000000 11111111.11111111.1 | 0000000.00000000
So the network 172.16.0.0 is divided into two networks,
  each network has 32768 total addresses of which 32766 are usable
    two are used in each subnet to represent the network address and broadcast address.
  The subnet mask for one bit subnetting is 255.255.128.0.
Class B – 1 bit subnetting

## Slide 17
Class B – 1 bit subnetting
SN No. | Description | Binaries | Decimal
1 | Network Address | 10101100.00010000.00000000.00000000 | 172.16.0.0
 | First address | 10101100.00010000.00000000.00000001 | 172.16.0.1
 | Last address | 10101100.00010000.01111111.11111110 | 172.16.127.254
 | Broadcast Address | 10101100.00010000.01111111.11111111 | 172.16.127.255
2 | Network Address | 10101100.00010000.10000000.00000000 | 172.16.128.0
 | First address | 10101100.00010000.10000000.00000001 | 172.16.128.1
 | Last address | 10101100.00010000.11111111.11111110 | 172.16.255.254
 | Broadcast Address | 10101100.00010000.11111111.11111111 | 172.16.255.255

## Slide 18
Class B – 2 bit subnetting
SN No. | Description | Binaries | Decimal
1 | NA | 10101100.00010000.00000000.00000000 | 172.16.0.0
 | 1st | 10101100.00010000.00000000.00000001 | 172.16.0.1
 | Last | 10101100.00010000.00111111.11111110 | 172.16.63.254
 | BA | 10101100.00010000.00111111.11111111 | 172.16.63.255
2 | NA | 10101100.00010000.01000000.00000000 | 172.16.64.0
 | 1st | 10101100.00010000.01000000.00000001 | 172.16.64.1
 | Last | 10101100.00010000.01111111.11111110 | 172.16.127.254
 | BA | 10101100.00010000.01111111.11111111 | 172.16.127.255
3 | NA | 10101100.00010000.10000000.00000000 | 172.16.128.0
 | 1st | 10101100.00010000.10000000.00000001 | 172.16.128.1
 | Last | 10101100.00010000.10111111.11111110 | 172.16.191.254
 | BA | 10101100.00010000.10111111.11111111 | 172.16.191.255
4 | NA | 10101100.00010000.11000000.00000000 | 172.16.192.0
 | 1st | 10101100.00010000.11000000.00000001 | 172.16.192.1
 | Last | 10101100.00010000.11111111.11111110 | 172.16.192.254
 | BA | 10101100.00010000.11111111.11111111 | 172.16.192.255

## Slide 19: Class A – 1 bit subnetting
Consider class A network 10.0.0.0 (subnet mask is 255.0.0.0)
If we include one bit from the host part to the network part, the subnet mask changes into 255.128.0.0.
The single bit can have two values in second octet, either 0 or 1 (so we can get two subnets with a single bit subnetting)
00001010.0 | 0000000.00000000.00000000 11111111.1 | 0000000.00000000.00000000
The network 10.0.0.0 is divided into two networks, each network has 8388608 total IPv4 Addresses and 8388606 usable IPv4 Addresses (two IPv4 Addresses are used in each subnet to represent the network address and the directed broadcast address).

## Slide 20: Class A – 1 bit subnetting
SN No | Description | Binaries | Decimal
1 | Network Address | 00001010.00000000.00000000.00000000 | 10.0.0.0
 | First IPv4 address | 00001010.00000000.00000000.00000001 | 10.0.0.1
 | Last IPv4 address | 00001010.01111111.11111111.11111110 | 10.127.255.254
 | Broadcast Address | 100001010.01111111.11111111.11111110 | 10.127.255.255
2 | Network Address | 00001010.10000000.00000000.00000000 | 10.128.0.0
 | First IPv4 address | 00001010.10000000.00000000.00000001 | 10.128.0.1
 | Last IPv4 address | 00001010.11111111.11111111.11111110 | 10.255.255.254
 | Broadcast Address | 00001010.11111111.11111111.11111111 | 10.255.255.255

## Slide 21: Class A – 2 bit subnetting
N No | Description | Binaries | Decimal
1 | Network Address | 00001010.00000000.00000000.00000000 | 10.0.0.0
 | First IPv4 address | 00001010.00000000.00000000.00000001 | 10.0.0.1
 | Last IPv4 address | 00001010.00111111.11111111.11111110 | 10.63.255.254
 | Broadcast Address | 00001010.00111111.11111111.11111111 | 10.63.255.255
2 | Network Address | 00001010.01000000.00000000.00000000 | 10.64.0.0
 | First IPv4 address | 00001010.01000000.00000000.00000001 | 10.64.0.1
 | Last IPv4 address | 00001010.01111111.11111111.11111110 | 10.127.255.254
 | Broadcast Address | 00001010.01111111.11111111.11111111 | 10.127.255.255
3 | Network Address | 00001010.10000000.00000000.00000000 | 10.128.0.0
 | First IPv4 address | 00001010.10000000.00000000.00000001 | 10.128.0.1
 | Last IPv4 address | 00001010.10111111.11111111.11111110 | 10.191.255.254
 | Broadcast Address | 00001010.10111111.11111111.11111111 | 10.191.255.255
4 | Network Address | 00001010.11000000.00000000.00000000 | 10.192.0.0
 | First IPv4 address | 00001010.11000000.00000000.00000001 | 10.192.0.1
 | Last IPv4 address | 00001010.11111111.11111111.11111110 | 10.255.255.254
 | Broadcast Address | 00001010.11111111.11111111.11111111 | 10.255.255.255